## Slide 2
Terapija pulpe i periapikalnih bolesti
Liječenje kanala se treba provesti u slučaju : - Nekroze pulpe ili ireverzibilnog pulpitisa - Vitalne pulpe (ali s lošom prognozom za vitalitet)
Kontraindikacije :
Pacijenti s visokim rizikom endokarditisa
Zubi s nefunkcionalnom budućnosti (osmice )
Zubi s neadekvatnom parodontnom potporom
ENDO basis

## Slide 3
Endo Basis
Usporedba tehnika
Manualna tehnika
  +: osjećaj
  +: manje rizika od perforacija
  -: potreban velik broj igala
  -: vremenski zahtjevno
  -: otežan pristup u stražnjim regijama
Rotirajuće tehnike
  +: brza preparacija kanala
  +: Auto-reverse
  - : zamor igala
Recipročne tehnike
  +: mali broj igala (1ručna , 1 mehanička igla )
  +: Sigurnost (lmanje lomova , manje apikalnog pritiska )

## Slide 4
Morfologije kanala
    Zakrivljeni / ravni
    veliki / mali
    Dugacki / kratki
Konicitet kanala
    10 % u koronarnom području , 2 to 4% u apikalnoj zoni
    Razlicite duzune
  najpopularnije
  21mm, 25mm, 29mm
  ostale 15mm, 19mm, 23mm
    Different diameters (ISO)
    Different tapers
    4%, 6%, 8%, 12%
Oblik iglica
+ radni vrsak rezan u smjeru kazaljke na satu i obrnuto od kazaljke na satu
)
Other shapes
Bibliography:
A la recherche des limes endodontiques idéales, Dr. Mc Spadden, Dental Tribune, 2009
Ø15 | Ø20 | Ø25 | Ø30 | Ø35 | Ø40
Endo basis

## Slide 5
Canal shaping
Otklanjanje pulpnog tkiva (etc)
=
Irigacija
(Sodium Hypochlorite 2,5%)
+
Inicijalna manuelna eksploracija
+
Mehanički shapeing sa irigacijom
- Crown Down tehnika (from the crown to the apex)
- Step-Back tehnika (from the apex to the crown)
+
Final irrigation: EDTA + Hypochlorite + drying
Obturation
Adaptacija master conea (glavne guttapeke ) finalnoj duzini
Biocompatibilni cement
Gutta-percha compaction + X-ray
Coronal obturation
Coronal restoration ASAP
ENDO protokol

## Slide 6
Prednost AUTO-REVERSE
The time from « x » to « y » must be as short as possible
(less than 1/1000 sec. )
Microprocessor analysis
Između x i y tork se povecava sve do max
Rotirajući instrumenti

## Slide 7
Manufacturer | Files | Protocol | Ncm | Speed Rpm
Dentsply VDW | ProTaper® Mtwo | Click to enlarge | 3 - 4 1 - 1.5 1.5 - 2 2- 3 3 - 4 2 - 3 1.5 - 2 | 250

## Slide 8
S1: Enlargement of the coronal and middle third S2: Enlargement of the middle third and apical third SX: Relocate the coronaries entries (can replace S1 and S2 files for short canals) F: Files dedicated to the finishing on the apical zone (different tip diameter and taper) Basic protocol (3 to 4 Protapers): 1. K10/K15 files for canal exploration 2. S1 to the manual file insertion length 3. Manual file to the apical third 4. S1 to the working length (WL) 5. S2 to the WL 6. F1 to the WL
ProTaper

## Slide 9
Ciklički zamor
 Igla se deformira zbog kompresije i tenzije pri pokretu u zakrivljenim kanalima File is deformed due to tension and
Torzija
Vrh igle je zaglavljen u kanali a tzv contra-angle se nastavlja rotirati .
Frakture

## Slide 10
Sigurnost: vrlo mali apikalni pritisak
 manji ciklički zamor (tension/compression)
   manje torzijskog zamora
Jednostavnost protokola
Efikasnost i brzina
Respektiranje anatomije kanala
Smanjen efekt deformacije igle
Reciročni pokreti
Major Advantages

## Slide 11
Single use
2 files brands dedicated to reciprocating motions are today existing:
- Wave one® from Dentsply Maillefer
Reciproc® from VDW:
more aggressive but also more fragile
Wave one /Reciproc®:
 Reverse helix
Fixed angulations:
150° REV - 30° FWD
Files - Reciprocating